## Slide 1: INTELLIGENT BUILDINGS (advantage,application)
Ar. Balraj Marjara

## Slide 2: Advantages
DDCs gather and store much more information from sensors, allowing for automated diagnosis of problems, more informed decisions on the part of facilities managers, and greater integration between systems.
Ability to either customize control sequences for a specific zone or to repeat control sequences in all zones of a building.
Increased precision and accuracy associated with digital controls.

## Slide 3: ADVANCED LIGHTING CONTROLS
Minimize lighting energy
use and optimize visual
comfort.
Accomplished with DDC’s
Zone DDC lighting control system

## Slide 4: Features
Photo sensor & Occupant sensor
Separate IP address
IP-addressed fixtures and sensors tied into the BAS allow both customized control of each fixture and building-wide lighting control

## Slide 5: Lighting Control Functions
Occupant Control of Lighting
  Productivity up 3%
  Tenant can access program through his PC
Scheduling
  Tenant occupancy schedules
Occupancy and Photo sensor controls

## Slide 6: EARTHQUAKE DAMPERS
MAGNETO-RHEOLOGICAL
FLUIDS
MR fluid inside the dampers
change from solid to liquid
and back as tremors activate
a magnetic force inside the
damper.
Create smart structures
that automatically react to seismic
activity.
MR Fluid Damper

## Slide 7: Application in Intelligent Buildings
DAMPERS
Classified into
  Passive
  Active
  Semi-Active
  A full- scale MR fluid damper that is 1 meter long and weighs 250kg. This one damper can exert 20 tons of force on a building.

## Slide 8: Building equipped with MR fluid dampers.

## Slide 9: Life Security System
Life safety factors involved in intelligent buildings include:
  Reduced manpower dependence
  Closed-circuit television
  Card access control
  Smoke detection
  Intrusion alarms
  Emergency control of elevators, doors
  UPS

## Slide 10
Advantages:
  Up to 30 percent lower capital costs due to ease of installation, consolidation of installation processes, and lower number of equipment panels
  Greater flexibility for changes and upgrades, leading to lower operating costs
  Less time required for tenant improvements phase due to prior installation of horizontal cabling
Objection :
  Pre-wiring of horizontal voice and data distribution systems adds cost for the building owner and may not fulfill the telecom expectations of the building tenants

## Slide 11
Advantages:
  Up to 30 percent lower capital costs due to ease of installation, consolidation of installation processes, and lower number of equipment panels
  Greater flexibility for changes and upgrades, leading to lower operating costs
  Less time required for tenant improvements phase due to prior installation of horizontal cabling
Objection :
  Pre-wiring of horizontal voice and data distribution systems adds cost for the building owner and may not fulfill the telecom expectations of the building tenants

## Slide 12
Intelligent buildings are
adaptable
Future Proofing
Adaptable for Tenant
Needs
Raised Access Floor

## Slide 13
THANK YOU