## Slide 1: Ar. Manish kumar
Projection of straight line

## Slide 2: PROJECTIONS OF STRAIGHT LINES
Definition of Straight line:
A straight line is the shortest distance between two points.
-Top views of two end points of a straight line, when joined, give the top view of the straight line.
-Front views of the two end points of a straight line, when joined, give the front view of the straight line.
-Both the above projections are straight lines.

## Slide 3: Orientation of Straight Line in Space
A line in space may be parallel, perpendicular or inclined to either the H.P. or V.P. or both.
It may be in one or both the reference Planes.
Line ends may be in different Quadrants.
Position of Straight Line in space can be fixed by various combinations of data like distance of its end points from reference planes, inclinations of the line with the reference planes, distance between end projectors of the line etc.

## Slide 4: Notatioans used for Straight Line
True length of the line:
Denoted by Capital letters. e.g. AB=100 mm, means that true length of the line is 100 mm.
Front View Length:
Denoted by small letters. e.g. a’b’=70 mm, means that Front View Length is 70 mm.
Top View Length:
Denoted by small letters. e.g. ab=80 mm, means that Top View Length is 80 mm.
Inclination of True Length of Line with H.P.:
It is denoted by θ. e.g. Inclination of the line with H.P. (or Ground) is given as 30º means that θ = 30º.

## Slide 5
two projectors of F.V. & T.V.
It is the distance between
passing through end points measured parallel to XY line.
Inclination of True Length of Line with V.P.:
It is denoted by Φ. e.g. Inclination of the line with V.P. is given as 40º means that Φ = 40º.
Inclination of Front View Length with XY :
It is denoted by α. e.g. Inclination of the Front View of the line with XY is given as 50º means that α = 50º.
Inclination of Top View Length with XY :
It is denoted by β. e.g. Inclination of the Top View of the line with XY is given as 30º means that β = 30º.
End Projector Distance:

## Slide 6: Line in Different Positions with respect to H.P. & V.P.
CLASS A: Line perpendicular to (or in) one reference plane & hence parallel to both the other planes
Line perpendicular to P.P. & (hence) parallel to both H.P. & V.P.
Line perpendicular to V.P. & (hence) parallel to both H.P. & P.P.
Line perpendicular to H.P. & (hence) parallel to both V.P. & P.P.

## Slide 7: Line in Different Positions with respect to H.P. & V.P.
CLASS B: Line parallel to (or in) one reference plane & inclined to other two planes
Line parallel to ( or in) V.P. & inclined to H.P. by .
Line parallel to ( or in) H.P. & inclined to V.P. by .
Line parallel to ( or in) P.P. & inclined to H.P. by  & V.P. by .

## Slide 8: Line in Different Positions with respect to H.P. & V.P.
CLASS C: Line inclined to all three reference planes ( Oblique lines )
Line inclined to H.P. by , to V.P. by  and also inclined to profile plane.

## Slide 9: Class A(1) : Line perpendicular to P.P. & hence parallel to both the other planes
P.P.
.
H.P.
V.P.
A
a’
b’
Y B
b
a
a”
b”
X
z
x
Y

## Slide 10: a’,. b’
V.P.
H.P.
Y
X
A
Y
B
a
b
Class A(2):Line perpendicular to V.P. &X(hence) parallel to both the other Planes
(i.e. H.P. & P.P.)

## Slide 11: Exercise 2 :- A Line ABC, 80mm long is perpendicular to V.P & 50mm below H.P. Point B, 20mm from A is
b
50
20
60
X
(2) AB = 20, BC = 60
(3) Point B is in V.P.
Y (4) Line is 50mm below H.P.
on V.P. A is in 4th quadrant. Draw the projections of
line ABC.
Data given :-
(1) T.L. = 80mm
Scale :- 1:1
- Point A is in 4th quadrant
.a’,b’,c’- Line is perpendicular to V.P.
.c
.a
.

## Slide 12
H.P.
a,b
.
V.P.
A
b’
B
a’
X
Y
Class A(3):Line perpendicular to H.P. & (hence) parallel to both the other Planes
Y
X