## Slide 1
Subject: Building Construction-IV
Topic: Stairs
Presented by: Atul Setya

## Slide 2
STAIRS

## Slide 3: Stair Detail

## Slide 4: Tread Detail
Minimum Going for domestic stairs is 220mm.
Maximum Rise is 220mm string and handrail.
In consecutive flights of stairs, each step shall have the same rise and the same going.
Handrail to be provided on both sides of stairs if width is 1.0 metres wide or more.

## Slide 5: Stair Terms
Stairwell
The space in which the stairs and landing are housed.
Tread
      Upper surface of a step on which the foot is placed
Riser
The vertical member between two treads
Step
Rise plus tread
Nosing
The exposed edge of tread usually rounded or splayed.

## Slide 6: Stair Terms
Handrail
Member parallel to the string and spanning between newels or fixed to the wall.
Baluster
      Vertical infill members between string and handrail.
Newel
Post at bottom and top of flight supporting handrail.
String
Members into which the ends of treads and risers are housed and wedged.
Pitch line
Line connecting the nosing of all treads in one flight.